## Slide 1: Source Approval Request (SAR) and Qualification Requirements Industry Training SASPO Industry Day
SAR Team
AFLCMC/LPE (Propulsion Engineering)
Email: AFLCMC.LPE.SourceEvalTeam@us.af.mil
DISTRIBUTION A Approved for Public Release; Distribution Unlimited. Destruction: 100% Shred

## Slide 2: BLUF
USAF WANTS to qualify YOU to manufacture and repair our parts !!!
  Increases competition and reduces sustainment costs
  Minimize qualification requirements while maintaining OSS&E (Operational Safety Suitability and Effectiveness)
USAF Seeking Focused SARs
  If we don’t need the parts, you won’t get a contract!

## Slide 3: Overview
MQR/RQR
Finding Tech Data
Company Profiles
SAR Categories
SAR Elements
Self-Assessment Checklist
Significant Industrial Process List
Cover Letter
Repair Capability/Source of Supply Matrix for Modules & Assemblies
Technical Data Rights Statement
Similar Item Comparison
Source Resubstantiation Request
Process Change Request
Document Submittal

## Slide 4: Propulsion Standard QRs
MQR-PSD-1
  Applies to CAT 1 & 2
RQR-PSD-1
  Applies to CAT 1, 2, 4, & 5
Comply with AFMCI 23-113, AFMCI 21-112, & SAM Handbooks
Find the QRs at the SASPO website:
- http://www.tinker.af.mil/Home/429SCMS-SASPO/

## Slide 5: Find Tech Data
Request Data or Data Rights Purchases for Drawings
  Public Sales Office (PSO) (405) 736-4676
  ocalc.lgldo.public@us.af.mil
  Provides commercial customers a method to purchase engineering data directly from the ALCs data repository.
  Requires the customer to register with FedBizOps prior to a purchase request.
    submit a request for data or ask questions through the PSO email listed below.
  Offers single or revolving account data purchase options.
  Department of Defense policy mandates only the Data Custodian listed on the Military Critical Technical Data Agreement (DD Form 2345) is eligible to receive data.
Technical Order Home Office
  aflcmc.ezgtp.pubsale@us.af.mil
  Provides commercial customers a method to purchase technical orders directly
  Department of Defense policy mandates only the Data Custodian listed on the Military Critical Technical Data Agreement (DD Form 2345) is eligible to receive data.
Prints
T.O.s
Process defined on SASPO Site

## Slide 6: Company Profile Requirements and Format
Each Company Profile must include the required data
The data requirements are defined by the QR elements
The 1221 is used to evaluate the data elements

## Slide 7: Company Profile Elements
Element 1: Company Brochure/Website
Element 2: Quality Assurance Certificate
  ISO 9001, AS9100, AS9110, or NATO-AQAP-2070
Element 3: Self-Assessment Checklist (see Appendix A)
Element 4: Quality Assurance System (QAS) Manual
Element 5: Equipment List
Element 6: DD Form 2345 or Export Control License
Element 7: Quality History

## Slide 8: Company Profile Elements
Element 8: Significant Industrial Process Certification
    Methods of certification include, but are not limited to, NADCAP, OEM, DOD (Air Force, DCMA, Navy, or Army certification and/or audit), or other external audit
    All methods will be reviewed by the ESA for process control and acceptability

## Slide 9: Company Profile Elements
Element 8: Significant Industrial Process Certification (cont.)
  Example:
    Signed Process Letter
    Actual Certs (as identified)

## Slide 10: Company Profile Elements
Element 9: Sub-Tier Supplier Info.
  List of all Sub-Tier Suppliers (STS)
  All STS Quality Assurance Certifications
  Any STS Significant Industrial Process Certifications

## Slide 11: Source Approval Categories
Category I, Actual Item. - This category covers PS who repair/manufacture the exact subject item, using OEM technical data, for the prime contractor, OEM, DOD, civil agency, foreign government, or the civil sector under Federal Aviation Administration (FAA).
Category II, Similar Item. - This category covers PS who have not previously repaired/manufactured the exact subject item, but have repaired/manufactured other items similar in material, coatings, design features, industrial processes, etc. for the prime contractor, OEM, DOD, civil agency, foreign government, or the civil sector under FAA. Multiple similar items may be used to demonstrate relevant experience. Similarity is not limited to aerospace applications.

## Slide 12: Source Approval Categories
Category IV, Pre-Developed Repair. - This category covers unsolicited SAR submittals by PSs who have a previously developed repair that has: been fully validated and verified, successfully performed on regular production parts, and those parts that have undergone the repair have had sufficient operational experience, including either AMT (Accelerated Mission Testing) or field operational use. This category will require all elements of a SAR Package and any additional information as determined by the ESA.
Category V, Developing Repair. - This category covers the PSs who have a repair, or could develop a repair, that will satisfy the need of the USAF in accordance with an advertised requirement. PS approval of a Category V SAR may still require repair verification, validation, and testing prior to complete approval of PS as an approved source. This category will require all elements of a SAR Package and any additional information as determined by the ESA.
For Repair Only (RQR-PSD-1)

## Slide 13: SAR Data Requirements and Format
Each SAR must be accompanied with the required data
The data requirements are defined by the QR elements
The 815 is used to evaluate the data elements

## Slide 14: SAR Elements
Element A: Cover Letter
Element B: Subject Item Technical
Element C: Proposed Production Documents
Element D: Sub-Tier Supplier List (Subject Item specific)
Element E: Significant Industrial Processes (Subject Item specific)
Element F: Calibrated Equipment List
Element G: Technical Data Rights Certification Statement
  Use newest copy in Appendix E

## Slide 15: SAR Elements
Element H: Licensee Agreement
Element I: Government Quality Assurance Compliance
Element J: Similarities/Differences Summary (N/A for Cat I SARs)
Element K: Similar Item Technical Data (N/A for Cat I SARs)
Element L: Demonstration Production Documents
Element M: Purchase Orders and Shipping Documents

## Slide 16: SAR Elements (Proposed Production Documents-Travelers)
Provide Actual Supplier’s complete detailed step-by-step procedural account
  Date, Name, and CAGE on top of the 1st Page
  A Page Number and Unique Document Number on every page
  For All Part Numbers
  Proper processing sequence
  Operation No., description, location, STSs, software data file name, etc.
  Each operation must include a stamp block to indicate accomplishment
Provide detailed proposed/actual op sheets for Traveler(s) process when required

## Slide 17: SAR Elements (Proposed Production Documents-Inspection Method Sheets)
Provide Actual Supplier’s complete detailed step-by-step procedural account
  Date, Name, and CAGE on top of the 1st Page
  A Page Number and Unique Document Number on every page
  For All Part Numbers
  Proper sequence necessary to inspect the subject item
  Must include expected and actual dimensions and units
  Pass/Fail dimensions are not acceptable, except when using Go-No-Go gauges
    Go-No-Go gauges must be included in Element F
  If a sampling plan is used, provide the sampling plan to be reviewed. Otherwise specify 100% inspection.

## Slide 18: Self-Assessment Checklist
Fill out Self-Assessment Checklist found in Appendix A
Must be signed by the Company President, Owner, or Plant Manager
(This image shows a small part of the actual Appendix)

## Slide 19: Significant Industrial Process List
Fill out Significant Industrial Process List found in Appendix B
(This image shows a small part of the actual Appendix)

## Slide 20: Cover Letter
Appendix C shows the information required in the SAR Cover Letter
(This image shows a small part of the actual Appendix)

## Slide 21: Repair Capability/Source of Supply Matrix for Modules & Assemblies
The table found in Appendix D is only necessary for modules/assemblies
(These images show a small part of the actual Appendix)
RQR-PSD-1
MQR-PSD-1

## Slide 22: Technical Data Rights Certification Statement
The current version of the TDRCS can be found in Appendix E
Must be signed by the Company President, Owner, or Plant Manager
(This image shows a small part of the actual Appendix)

## Slide 23: Similar Item Comparison
A sample comparison matrix can be found in Appendix F
(This image shows a small part of the actual Appendix)

## Slide 24: Source Resubstantiation Request (SRR)
Only an Approved Source that has produced a CSI within three (3) years or
a CAI within seven (7) years can submit a PCR/SRR
If a source is currently producing and delivering for the USAF, there is no need for re-substantiation
  If a source stops production and within three (3) years for CSI or seven (7) years for CAI from the last time the item was produced by that source, the source may re-substantiate. If a PS lapses past this timeframe, a full SAR submittal will be required for approval
An approved source that has not delivered the subject item(s) to the USAF may re-substantiate within three (3) years for CSI and seven (7) years for CAI from the time of qualification. If a PS lapses past this timeframe, a full SAR submittal will be required for approval.

## Slide 25: Process Change Request (PCR)
After becoming a qualified source:
  If a change to your process is required affecting an aspect of your submitted SAR such as changing:
    Sub-tier Suppliers
    Raw Material Suppliers
    Any Industrial Process
    Travelers/Process Operation Sheets
    Inspection Method Sheets
    Machine Location
  To remain qualified, the ESA must be informed of and approve these changes
    Send a process change request listing everything that has changed
    Add any applicable documentation
    The ESA may ask for further information/documentation

## Slide 26: Source Resubstantiation Request (SRR) / Process Change Request (PCR)
(This image shows a small part of the actual Appendix)
The PCR/SRR Form can be found in Appendix G

## Slide 27: SAR Resources
Small Business Office
Liaison between Government and all businesses
- http://www.afsc.af.mil/Units/SBO.aspx
SASPO
Strategic Alternate Sourcing Program Office
- RPOW/Target List
- AFMCI 23-113/AFMCI 21-112
- Qualification Requirements
- http://www.tinker.af.mil/Home/429SCMS-SASPO/
SAM
System for Award Management
- Find the NSN(s) from the target list
- Bidding info / dates
- https://beta.sam.gov
Focus your SARs / Get Help

## Slide 28
Questions?